## Slide 1: Estimating high-resolution profiles of wind speeds from a global reanalysis dataset using TabNet
Harish Baki, Geosciences and Remote Sensing, Faculty of Civil Engineering & Geosciences, TU Delft
Sukanta Basu, Atmospheric Sciences Research Center, University at Albany

## Slide 2: Background
Ever growing offshore turbine heights pose challenges
Traditional hub height wind speed in estimating power output fails, due to inconsistent wind shear at across the rotor plane. Rotor equivalent wind speed approach is inevitable
Tip of a turbine can penetrate deep into the atmospheric boundary layer (ABL), where winds vary with height
Distinct types wind profiles
Significant influence of atmospheric stability parameters (wind shear and turbulence intensity) on wind power estimation and turbine loading
Underscores the importance of characterizing wind profiles

## Slide 3: Problem Statement
Challenges in estimating wind profiles across rotor plane
Scarcity of tall tower datasets
Extrapolation of surface measurements using similarity theory-based and/or empirical equations
  logarithmic law of the wall
  Monin-Obukhov similarity theory
  Power law
Mesoscale models - Expensive
ML models extrapolating near surface winds to specific rotor-swept heights
  Deep Neural Networks
  Random Forest
  Extreme Gradient Boosting (XGBoost)
Proposed Methodology
Provided large-scale meteorological features from ERA5, is it possible to estimate wind profiles using a DL model?
Methodology invariant to target dataset through the utilization of Chebyshev polynomial approximation
State-of-the-art TabNet, an attention-based sequential deep learning model
To mimic the measure-correlate-predict (MCP) approach, train the DL model for one year and predict for another
Assess the correlation of wind profiles with associated atmospheric conditions

## Slide 4: Data
As a proof-of-concept
34 ERA5 reanalysis meteorological features as inputs
CERRA reanalysis wind speed data at 12 vertical levels: 10, 15, 30, 50, 75, 100, 150, 200, 250, 300, 400, and 500 meters above sea level as targets
Point-based time-series data at FINO1 site (54.0143N, 6.58385E), well known for several wind meteorological studies
Data during 0000UTC on 1st of Jan 2000 to 2300UTC on 31st of Dec 2021

## Slide 5: Estimating Chebyshev coefficients
Wind speed (U) as a function of height (z) can be approximated using Chebyshev polynomials as
- Chebyshev polynomials
4th order Chebyshev polynomials
- Chebyshev coefficients, estimated through solving system of linear equations or inverse matrix multiplications

## Slide 6: TabNet
No explicit normalization is necessary
Identical steps repeated for decision steps
- width of decision prediction layer
- width of attention embedding layer

## Slide 7: TabNet
FT
  Several GLU blocks
  - number of shared GLU blocks, shared across decision steps
  - independent GLU blocks
  At each , it splits output into prediction and next step attention
  Input size:
  Output size:

## Slide 8: TabNet
AT:
  Priors of features
  Initialized with 1
  In the subsequent steps, it is
  Large allows reusage of same features at every step, while small gamma uses different features at each step
  Input size:
  Output size:

## Slide 9: TabNet
No explicit normalization is necessary
Identical steps repeated for decision steps
- width of decision prediction layer
- width of attention embedding layer
Model parameters: , , , , , and

## Slide 10: Experimental setup

## Slide 11: Results

## Slide 12: Results